### Q1
A Software Defined Network, SDN, is a network whose Control Plane is separated from it’s Data Plane through software making a network configurable through Application Programmable Interfaces, APIs rather than having to physically connect to possibly hundreds of switches and routers to configure them.
### Q2
Continuing this configuration is done by an SDN controller which manages the entire networks forwarding decisions/schemes. The SDN controller is the software that the network administrator< uses.
### Q3
An SDN switch is a a switch that runs a SDN protocol like OpenFlow and is configurable by an SDN controller. These can be pure SDN switches that is fully reliant on SDN, Hybrid that runs both SDN and traditional swicthing configuration and Virtual Switches (vSwitch) that are fully software-based switches that resides strictly in cloud and virtualized environments.
### Q4
Match-plus-action is an SDN principle whilst desitination-based routing is a traditional principle. Destination-based routing means that packets that are forwarded in a router or switch are based only on it’s destination IP adress that is matched with the switch MAC table or routers routing table. Match-plus-action examines packets incoming and can match them against rules that now can have multiple attributes and after rules are applied performs an action like forward, drop or modify. It can apply priority, ports firewall rules filtering etc all since the Data Plane, control plane and management plane now is abstracted.
### Q5
### Q6
### Q7
### Q8

### Q9

### Q10
### Q11

### Q12

The reason is that as of yet we have no flow rules to determine routes inside the network so packets are by default dropped due to the lack of rules.
### Q13
### Q14

### Q15
Cookie =0x0 means no cookie was attached meaning the flow rule it’s not set up to be modified elsewhere.
Duration is how long the flow rule has been active
Table=0 means these flow rules are the first entry in the table of flow rules.
n_packets is a value of how many packets have been matched with the specific rule
n_bytes is how many bytes have been matched with the specific rule
priority, which we set to 1 in the config line, is applied when there are multiple rules that apply to a packet. Priority 1 is low the rule with the highest priority is the one that is going to apply.
in_port is the port on the switch where the rule applies for in coming packets. We specified this with alias names 1 and 2 in the command line and here their full name is viewed.
Actions is where the rule applies it’s action(drop,forward etc.) on. In this case it’s to forward(output) to the other rules in-port.
### Q16

It works now since the flow rules have port forwarded outputs to corresponding inputs of the hosts.
### Q17

No, ping packets dropped and as you can see the output of the dpctl del-flows is a dump of the flows which shows there are none. Del-flows also suspiciosly looks like an abbreviation of delete flows.
### Q18

OpenFlow Protocol Type, OFPT: Hello, Features Request and Reply, Multipart Message Port Descriptions Request and Reply as well as a Flow Modifyer (add, modify or delete flow entries).
### Q19

The FLOW_MOD message adds a flow entry.

The first ping was slower due to the time needed for configuration of flow.

OpenFlow Extensible Match, OXM, fields specify input port of the switch, source MAC and destination MAC. The instruction field explains the action the flow rule is supposed to apply OpenFlow Protocol Action Type, OFPAT, which is output(forward). To the right is the cookie info, Table ID and Priority(1). This is the info we set manually before and got as the output of the flow dump.
### Q20

ARP frames.
### Q21
ARP aims to find the Media Access Protocol, MAC, address of the device that has a specific IP address and then return that MAC address to the IP address of who asked for it. The ARPs corresponds to the packets since it never gets to know the MAC address due to no flow rules and therefore keeps asking.

### Q22
The problem is when a switch recieves a broadcast from a switch and then broadcast the same request if the first switch were to broadcast again we would have an infinite loop and therefore if a switch has broadcast a request it should have only handle the request and then drop each echoed request.

### Q23

Now ARP traffic going from switch to switch dies out when it reaches the host connected switches.
### Q24

It behaves as expected. It handles the Address Resolution but since ping uses ICMP which isn’t ARP frame but an Internet Protocol datagram it gets automatically dropped.
### Q25

It maps IP addresses with their respective MAC addresses on a specific link in this case the hosts ethernet-links.
### Q26

Relevant commands are: Priority=5 which is lower than ARP priority to not disturb ARP communications functionality. Ip to target Internet Protocol traffic (non Data Link only traffic like ARP). nw_src to set which link a host of that source IP address should use and nw_dst to match packets with a certain destination ip address to it’s respective port. I only specify which link a certain host uses and does not restrict which destination it uses since the specifications do not require a restrictive links I choose to keep possibilities open and perform restrictions later. Scalability.
### Q27

Between 1.76 and 3.48 Mbits/sec
### Q28

Average latency is 347ms since packet has to travel over the high latency link 2*150ms + 2*10ms = 320ms which also is almost the reported minimum latency (326ms).
### Q29

Relevant commands are the same as Q26.
### Q30

Between 0.682 and 1.56 Mbit/sec.
### Q31

Latency is about 10ms which is about right. 2*3ms = 6ms. The rest of the 4ms is the switching delay which can be seen in the discrepancy of Q28 where propagation-delay = 320ms and the real delay=326ms: 320-326=6ms switching delay. 6ms/3switches = 2ms/switch. 2ms * 2 switches = 4ms which confirmes the observation.
### Q32

No host is connected to it’s “network neighbor” only to the other network.
### Q33

Yes I can ping h1 from h3. Lowest latency is 168ms. h3 sends ICMP request over link 3; 3ms. h1 sends ICMP response over link 5/4; 150+10=160ms. 160+3+switch-delay≈168ms. Throughput = 64*8/168=3047.6bps
### Q34

No it does not change anything. As it shouldn’t. H1 is configured to communicate via ip on link 5/4 no matter what and h3 on link 3.
### Q35

Relevant commands are: hard_timeout which specifies after how much time a flow rule will be active. Priority 65535 is the highest priority according to the man-page which makes the firewall definitive.
### Q36

h1 → h4 is blocked for 300 seconds as expected and all packets are dropped at s1.
### Q37

h4 → h1 is blocked for 300 seconds as expected and all packets are dropped at s2.
### Q38

Only h1 → h4 and h4 → h1 changed as expected. Since only ip packets with {src:10.0.0.1 AND dst:10.0.0.4} OR {src:10.0.0.4 AND dst:10.0.0.1} are dropped. Switch is treating the matches with logical AND. If packets from src:10.0.0.1 OR src:10.0.0.4 have any other destination the firewall does not apply. This also has highest priority and thats why it’s chosen over previous flow rules.

### Whole flow configuration